RR-duino protocol

Structure : Start byte, command byte, address (1 byte) [,subaddress (1 byte), parameters…]

Header bytes
Start byte
B7-B0	Value = FF
Command byte
B7-B3	B7=0 : « R/W » command : / B4=0:Read command / B5=0 : read from sensor(s) / B6=0:from certain sensors (subaddresses follow, see below) / B6=1:from all sensors / B5=1 : read from turnout(s) / B6=0:from certain turnouts (subaddresses follow, see below) / B6=1:from all turnouts / B4=1 : Write command / B5=0 : write to sensor(s) / B6=0:to certain sensors (subaddresses follow, see below) / B6=1:to all sensors / B5=1 : write to turnout(s) / B6=0:to certain turnouts (subaddresses follow, see below) / B6=1:to all turnouts / B7=1 : « Config/Other » command : / B3=0 : normal config / B4=0:Sensor config / B4=1 : Turnout config / B3=1 : « special » config or other commands / B6-B5 : 00 => version / B6-B5 : 01 => Set address / B6-B5: 10 => Show command / B4 : 0 => sensors 1=> turnouts / B6-B4 : 110 => Turnout fine tuning / B6-B4: 111 => Clear EEPROM
B2	B2=1 : from Master :asks the slave to send any pending messages originating from the slave (like turnouts having reached its position, an input sensors that has changed value,…), then B7-B3=max number of answers to be sent by the slave / B2=1 : from slave, 2 cases : / if it is in the last answer to a command from the master (B1 must be 0 then), it means there are async events waiting to be sent by the slave (like turnouts having reached its position, an input sensors that has changed value,…) / when it is in response to the master asking to send the async events / otherwise B2=0
B1-B0	B0=1 : command from the master / B1=0 (ensures that the command byte is never 0xFF) / B0=0: answer from the slave / B1=0 : no other answer pending / B1=1 : Other answer(s) pending
Address byte
B7	Reserved, must be 0 for now
B6	B6=0 : only one subaddress follows (simple command) / B6=1 : several subaddresses follow or none in the case of all sensors/turnouts read/write
B5-B0	Address (1-62) (not 63 to avoid being 0xFF)

Payload bytes
Subaddress byte
B7	B7=1 means last subaddress in a list (see below), in that case B6-B4=000 / and B3-B0=error code (0 meaning no error) / B7=0 : subaddress in B5-B0 (if in a list, it is not the last one)
B6	Value to write (see turnouts/sensors write command below) / or read value (see turnouts/sensors write command below) / or for turnout config : / B6=1 <=> relay pin present, 0 otherwise / or for sensor config : / B6=0 : input sensor / B6=1 : output sensor
B5-B0	Subaddress (1-63)
Pin byte
B7	For input sensor config : / B7=0 : no pull-up / B7=1 : pull-up / For the relay pins in a turnout config : / B7=0 : drive the pin continuously (normal relay) / B7=1 : pulse the pin (~10ms, for latching relay)
B6-B0	Pin number : 1-126 (not 127 to avoid 0xFF value)

Every command/answer is limited to a total of 64 bytes.
Specific commands and their corresponding answers :

1. R/W commands/answers
  1. Read sensor/turnout commands : (command[B1-B0]=01)
  You can read any sensor ; input obviously but also output as you get the current state, same for a turnout.
  start byte, command (byte), address (byte)[, subaddress1 (byte), subaddress2(byte)…];
  Payload :
  if command[B6]=address[B6]=0 : only one sensor/turnout, so only subaddress1
  if command[B6]=0 and address[B6]=1 : several subaddresses follow
    subaddress1,subaddress2,…,subaddress_last, 0x80
  if command[B6]=1 (all sensors or all turnouts)
    no payload
  1. Read sensor/turnout answers : (command[B0]=0, command[B1] indicates if other answers are pending (for this command or « spontaneous » answers like an input changed)
start byte, command (byte), address (byte)[, subaddress1 (byte), subaddress2(byte)…]|[string of byte (see below)];
Payload :
if command[B6]=address[B6]=0 : only one sensor/turnout : subaddress1 | 0x8x (x=0 :no error otherwise error « number x »)
  if command[B6]=0 and address[B6]=1 : several subaddresses follow
    subaddress1,subaddress2,…,subaddress_last, 0x8x (x=0 :no error otherwise error « number x »)
    if command[B6]=1 (all sensors or all turnouts) :
1. string of bytes made from the read values (1 bit each), all bytes have their MSB=0 the last byte is 0x8x (x=0 : no error otherwise error « number x »)
    it is assumed that the sensors/turnouts we are reading from are in increasing subaddress order: the 7th bit of the first byte will be read from the sensor/turnout of lowest subaddress and so on...
  2. Write sensor (output sensor only)/turnout commands :
  start byte, command (byte), address (byte)[, subaddress1 (byte), subaddress2(byte)…]|[string of byte (see below)];
Payload :
  if command[B6]=address[B6]=0 : only one sensor/turnout, so only subaddress1
  if command[B6]=0 and adress[B6]=1 : several subaddresses follow
    subaddress1,subaddress2,…,subaddress_last, 0x80
if command[B6]=1 (all sensors or all turnouts)
string of bytes made from the values (1 bit each) to write, all bytes must have their MSB=0 the last byte has its MSB=1 (but is not 0xFF)
it is assumed that the sensors/turnouts to write to are in increasing subaddress order: the 7th bit of the first byte will be written to the sensor/turnout of lowest subaddress and so on…
  1. Write sensor (output sensor only)/turnout answer :
1. start byte, command (byte), address (byte), 0x8x (x=0:no error, otherwise error « number x »)
2. Normal config commands :
  1. Sensor config
  start byte, command (byte), address (byte), subaddress1 (byte), pin number1 (byte)[, subaddress2 (byte), pin number2 (byte), ...]
  This is use to set a new sensor or update an existing one.
  If address[B6]=0 : only one sensor, so only subaddress1,pin number1
  If address[B6]=1 : several subaddresses follow
  subaddress1, pin number1,subaddress2 pin number2,…,last subaddress, last pin_number  ,0x80
  1. Sensor config answer :
  start byte, command (byte), address (byte), 0x8x (x=0:no error, otherwise error « number x »)
  1. Turnout config
  start byte, command (byte), address (byte), subaddress (byte), servo pin number (byte), straight pos (byte), thrown pos (byte)[, relay pin 1 (byte), relay pin 2 (byte)]
  Same as for sensors (as per only one turnout or several). The presence of relay pins is indicated in the subaddress[B6] bit.
  1. Turnout config answer
  start byte, command (byte), address (byte), 0x8x (x=0:no error, otherwise error « number x »)
3. Set address:
  1. command
  start byte, command (byte), address (byte)
  Remark : only a slave with its ADDRESS_MODE pin held to low will pick this message (and there should be only one on the bus at the time),
  1. answer
  start byte, command (byte), address (byte),0x8x (x=0:no error, otherwise error « number x »)
4. Get version :
  start byte, command (byte), address (byte)
5. Clear eeprom :
  start byte, command (byte), address (byte)
6. Show commands/answers (sensors/turnouts) :
  1. Show commands
  start byte, command (byte), address (byte), max number of config in the answer (byte)
  0 for max number of config means no limit (see answer to this command for more explanations)
  1. Show answers
    For sensors :
  start byte, command (byte), address (byte), subaddress1, pin1 [, subaddress2, pin2,…], 0x8x (x=0:no error, otherwise error « number x »)
  For turnouts :
  start byte, command (byte), address (byte), subaddress1, servo pin1, straight pos1, thrown pos1 [, relay pin1 1, relay pin1 2] [, subaddress2, servo pin2, straight pos2, thrown pos2 [, relay pin2 1, relay pin2 2], …],0x8x (x=0:no error, otherwise error « number x »)
7. Turnout fine position tuning :
  1. command
  start byte, command (byte), address (byte), subaddress, position
  position is a number between 1 and 180 (most servos will choke on extreme positions, so probably better to stay between 10 and 170).
  Position = 0 means end of fine tuning, detach servo.
  1. answer
  start byte, command (byte), address (byte), 0x8x (x=0:no error, otherwise error « number x »)
8. Send async events command :
  This is used by the Master to ask the slave to send any pending async events, for example if an (or several) input sensor(s) has/have changed its/their values or a turnout has reached its final position.
  Master command :
  start byte, command (byte), address (byte)
  command[B2]=1, command[B7-B3]=limit (0 means no limit)
  Slave answer : normal answer from the slave (with all command bits sets according to the event being sent, for example if an (or several) input sensor(s) has/have changed its/their values, the command bits must be set as if it was a read sensor command, same for a turnout reaching its final position) and command[B2]=1

IMPORTANT NOTE : no other byte than the start byte can be 0xFF.

Examples of exchanges :

- Master→Slave :Write command
- Master→Slave : Read command
  Slave →Master : Read answer (answer bit set, if there are more answers that was allowed in the read command or other answers are pending, then command[B1] bit is set)
  The master must repeat the same command while the other answers pending bit is set (command[B1]=1) and command[B2]=0 (meaning the pending answers are related to the original command).
- In case an answer from the slave to a command from the master has command[B1]=command[B2]=1 that means there are pending async messages from this slave, in that case the master has to send a command with only command[B2]=1 to enable the slave to send them :
- Master → Slave : send async event command
  Slave→ Master : normal answer with command[B2]=1 (respect also the limit set by the master in the command byte)